## Slide 1: Lecture Notes for Logic Family
1

## Slide 2: OVERVIEW
Introduction
Logic Family Classification
Fan IN And Fan Out
Noise Margin
Transistor as a Switch
RTL, DTL, TTL and ECL
Elementary data of CMOS
2

## Slide 3: Introduction
3
Logic families represent kind of digital circuit/methodologies for logic expression.
Integration levels :
SSI: Small scale integration MSI: Medium scale integration LSI: Large scale integration VLSI: Very large scale integration
12 gates/chip
100 gates/chip
1K gates/chip 10K gates/chip
ULSI: Ultra large scale integration
100K gates/chip

## Slide 4: Classification
Logic Family
Bipolar Logic Family
Saturated
Non Saturated
RTL(resistor transistor logic)
DCTL(direct coupled transistor logic) IIL(integrated injection logic) DTL(diode transistor logic)
HTL(high threshold logic)
TTL(transistor transistor logic)
Schottky TTL
ECL(emitter coupled logic)
ULF(unipolar logic family)
PMOS(p-channel MOSFET) NMOS(n-channel MOSFET) CMOS
4

## Slide 5: Fan In
Fan in or gate is the number of inputs that can practically be supported
without degrading practically input voltage level.
Fan in = 4
Fan Out
The maximum number of digital input that the output of a single logic
gate can feed and the gate must be same logic family.
Fanout = 4
Fan Out is calculated from the amount of current available in the output of a gate and the amount of current needed in each input of the connecting gate.
It is specified by manufacturer and is provided in the data sheet.
Exceeding the specified maximum load may cause a malfunction because the circuit will not be able supply the demanded power.

## Slide 6: Noise Margin
Noise is present in all real systems. This adds random fluctuations to voltages representing logic levels.
Hence, the voltage ranges defining the logic levels are more tightly constrained at the output of a gate than at the input.
Small amounts of noise will not affect the circuit. The maximum noise voltage that can be tolerated by a circuit is termed its noise immunity (noise Margin).

## Slide 7: Propagation Delay

## Slide 9: Transistor as a switch
A circuit that can turn on/off current in electrical circuit is referred to a switching circuit and transistor can be employed as an electronic switch.
Cut off region - OFF State
Both junctions are reverse biased, Ic = 0 and V(BE) < 0.7 v
Saturation region - ON State
Ic = maximum and V(BE)>0.7 v

## Slide 10: Resistor Transistor Logic(RTL)
The basic RTL device is a NOR gate.
The inputs represent either logic level HIGH (1) or LOW (0).
The logic level LOW is the voltage that drives corresponding transistor in cut-off region, while logic level HIGH drives it into saturation region.
If both the inputs are LOW, then both the transistors are in cut-off i.e. they are turned-off. Thus, voltage Vcc appears at output I.e. HIGH.
If either transistor or both of them are applied HIGH input, the voltage Vcc drops across Rc and output is LOW.

## Slide 11: Advantages of RTL Logic circuit:
The primary advantage of RTL technology was that it involved a minimum number of transistors, which was an important consideration before integrated circuit technology, as transistors were the most expensive component to produce
Limitations:
The obvious disadvantage of RTL is its high current dissipation when the transistor conducts to overdrive the output biasing resistor. This requires that more current be supplied to and heat be
removed from RTL circuits. In contrast, TTL circuits minimize both of these requirements.•
(NOR GATE USING RTL)

## Slide 12: Diode Transistor Logic
The diode-transistor logic, also termed as DTL, replaced RTL family because of greater fan-out
capability and more noise margin.
DTL circuits mainly consists of diodes and transistors that comprises DTL devices.
The basic DTL device is a NAND gate.
Two inputs to the gate are applied through diodes viz. D1, D2 . The diode will conduct only when corresponding input is LOW.
If any of the diode is conducting i.e. when at least one input is LOW, the voltage at output keeps transistor T in cut-off and subsequently, output of transistor is HIGH. If all inputs are HIGH, all diodes are non-conducting, transistor T is in saturation, and its output is LOW.
.

## Slide 13: Due to number of diodes
(Block Diagram of DTL)
used in this circuit, the speed of the circuit is significantly low. Hence this family of logic gates is modified to
transistor-transistor logic i.e.
TTL family which has been discussed on next slide.
(DL AND GATE)
(SATURATING
INVERTER)
D1
D2

## Slide 14: Transistor Transistor Logic
TTL family is a modification to the DTL. It has come to existence so as to overcome the speed limitations of DTL family. The basic gate of this family is TTL NAND gate.
Q3 is cutoff (act like a high RC ) when output transistor Q4 is saturated and Q3 is saturated (act like a low RC ) when output transistor Q4 is cutoff . Thus one transistor is ON at one time.
The combination of Q3 and Q4 is called TOTEM POLE arrangement.
Q1 is called input transistor, which is multi emitter transistor, that drive transistor Q2 which is used to control Q3 and Q4.
Diode D1 and D2 are used to protect Q1 from unwanted negative voltages and diode D3 ensures when Q4 is ON, Q3 is OFF.

## Slide 15: The output impedance is asymmetrical between the high
and low state, making them unsuitable for driving transmission lines. This drawback is usually overcome by buffering the outputs with special line-driver devices where signals need to be sent through cables. ECL, by virtue of its symmetric low-impedance output structure, does not have this drawback.
15
( BLOCK DIAGRAM OF TTL)

## Slide 16: Emitter Coupled Logic
ECL logic family implements the gates in differential amplifier configuration in which transistors are never driven in the saturation region thereby improving the speed of circuit to a great extent. The ECL family is fastest of all logic families.
Based on BJT, but removes problems of delay time by preventing the transistors from saturating.
Very fast operation - propagation delays of 1ns or less.
Low noise immunity of about 0.2-0.25 V .
The input impedance is high and the output impedance is low. As a result, the transistors change states quickly, gate delays are low, and the fan out capability is high.

## Slide 17: (FUNCTION TABLE)
•
(Block Diagram of ECL)
(ECL 2 INPUT OR/NOR GATE)
(LOGIC SYMBOL)
(TRUTH TABLE)

## Slide 18: Complimentary MOS (CMOS)
Considerably lower energy consumption than TTL and ECL, which has made portable electronics possible.
Most widely used family for large-scale devices
Combines high speed with low power consumption
Usually operates from a single supply of 5 – 15 V
Excellent noise immunity of about 30% of supply voltage
Can be connected to a large number of gates (about 50) .

## Slide 19: Transistors as Switches
We can view MOS transistors as electrically controlled switches.
Voltage at gate controls path from source to drain

## Slide 20: CMOS Inverter
A | Y
0 | 
1 | 

## Slide 21: CMOS Inverter
A | Y
0 | 
1 | 0

## Slide 22: CMOS Inverter
A | Y
0 | 1
1 | 0

## Slide 23: CMOS NAND Gate
A | B | Y
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 24: CMOS NAND Gate
A | B | Y
0 | 0 | 1
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 25: CMOS NAND Gate
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 
1 | 1 | 

## Slide 26: CMOS NAND Gate
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 

## Slide 27: CMOS NAND Gate
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 28: CMOS NOR Gate
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 29: 3-input NAND Gate
Y pulls low if ALL inputs are 1
Y pulls high if ANY input is 0

## Slide 30: 3-input NAND Gate
Y pulls low if ALL inputs are 1
Y pulls high if ANY input is 0

## Slide 31: Some statistical characteristics data of different logic families

## Slide 32: References
Switching Circuit and Logic Design by Prof. Indranil Sengupta, IIT KGP
Modern digital Electronics by R P Jain
NPTEL VIDEO by Dr. Amitava Dasgupta, IITM
Logic Families by Dr. Basem Elhalawany
Logic Gates and Family by Dr. A. P. VAJPEYI, IITG
Thank You